## Slide 1: CMPE 220
Class 3
Computer Architecture
Simplified Instructional Computer
Notes: Let’s talk about history.
California State Railroad Museum – 1976 - docents worked on original steam engines.

## Slide 2: Simplified Instructional Computer (SIC)
A hypothetical computer that includes the hardware features most often found on real machines.
  SIC (standard model)
  SIC/XE
Upward compatible
  Programs for SIC can run on SIC/XE
SIC is a good example of the basic architectural features required in a computer.
I’ll use SIC for many of the examples in the remainder of this class

## Slide 3: SIC - Memory
8-bit bytes
3 consecutive bytes form a 24-bit word
  Words are addressed by the lowest number byte
215 (32768) bytes in the computer memory

## Slide 4: SIC - Registers
Five 24-bit registers
Mnemonic | # | Use
A | 0 | Accumulator: used for arithmetic & logic operations
X | 1 | Index: used for addressing
L | 2 | Linkage: stores the return address for a subroutine jump. Only allows one level of return. SIC does not have a stack.
PC | 8 | Program Counter: contains the address of the next instruction to be fetched
SW | 9 | Status Word: see next page

## Slide 5: SIC – Status Word (SW)
Field | Length (bits) | Bits | Use
mode | 1 | 0 | user mode (0) or supervising mode (1)
state | 1 | 1 | process is in running state (0) or idle state (1)
id | 3 | 2-5 | process id (PID)
CC | 2 | 6-7 | condition code (device state)
mask | 4 | 8-11 | interrupt mask
X | 4 | 12-15 | (unused)
icode | 8 | 16-23 | interrupt code i.e. Interrupt Service Routine

## Slide 6: SIC – Instruction Format
24 bits (1 word)
opcode: machine instruction code (8 bits)
m: address mode (1 bit)
  0: direct
  1: indexed (aka base register addressing)
address: target address, or offset from X register (15 bits)
opcode
m
address

## Slide 7: SIC – Addressing Modes
Direct
Indexed (Base Register addressing)
opcode
0
address
Operand
Memory Location
opcode
1
address
Address
Operand
Memory Location
X Register
Effective address
+

## Slide 8: SIC – Data Formats
Characters: 8-bit ASCII
Integers: 24-bit binary, two’s complement
No decimal, no floating point

## Slide 9: SIC – Instructions (Load & Store)
Transfer 1 word of data (24 bits) between the A, X, or L registers, and a memory location
Transfer 1 byte of data (8 bits) between the A register, and a memory location
  STA location
  STL location
  STX location
  LDA location
  LDL location
  LDX location
  LDCH location
  STCH location

## Slide 10: SIC – Instructions (Arithmetic & Logic)
Arithmetic involves the A register and a memory location
  ADD location
  SUB location
  MUL location
  DIV location
  AND location
  OR location
The contents of the A register are replaced by: A (operation) (contents of location)

## Slide 11: SIC – Instructions (Comparison)
Comparison instructions set the CC flag to <, =, or >
Compare the A register and the contents of a memory location
  COMP location
Increment the X (index) register, and compare the result to the contents of a memory location
  TIX location

## Slide 12: SIC – Instructions (Jump)
Unconditional Jump
  J location
Conditional Jumps (based on value of CC flag):
  JEQ location
  JLT location
  LGT location
Jump to subroutine; store return address in L register
  JSUB location
Return from subroutine (jump to address in L register)
  RSUB

## Slide 13: SIC – Input/Output
Three I/O instructions
TD: Test Device; returns status in CC flag of SW register. ‘<‘ means ready, ‘=‘ means not ready.
RD: Read one byte of data from the specified device into the lower 8 bits of the A register.
WD: Write one byte of data from the lower 8 bits of the A register to the specified device.

## Slide 14: SIC – A Workable RISC Instruction Set
Although lacking many “convenience” instructions, the SIC architecture implements a fully functional, general purpose instruction set, similar to common minicomputers of the 1960s.
Its chief limitation is the 15-bit address space, allowing only 32,767 bytes of memory.

## Slide 15: Non-Instruction Statements (SIC)
So far, we’ve talked about statements that correspond one-to-one to machine code instructions… but there is another statement type required: the memory declaration.
Reserve some memory, and assign a label: inventory RESW 5 (Reserve 5 words) partnumbers RESB 100 (Reserve 100 bytes)
Reserve some memory, and assign a label and starting value: inventory WORD 100 (Reserve 1 word; value=100) partname BYTE C‘widget’ (Reserve 6 bytes; value=‘widget’) Iochannel BYTE X‘05’ (Reserve 1 byte; value=x05)

## Slide 16: Other Housekeeping Statements
Indicated starting address of program: programname START 1000
Indicate end of program, and location of first statement: END starthere

## Slide 17: SIC/XE – An Extended CISC Instruction Set
The SIC/XE is fully backward compatible with the SIC. That is, it will run all SIC instructions.
It adds:
  A 20-bit addressing mode, supporting 1 MB of memory
  Floating point arithmetic
  Multiple new addressing modes
  Additional arithmetic and logic functions

## Slide 18: SIC/XE – Additional Registers
Mnemonic | # | Use
B | 3 | Base: base register for addressing
S | 4 | S: general accumulator
T | 5 | T: general accumulator
F | 6 | F: floating-point accumulator (48 bits)

## Slide 19: SIC/XE – Additional Instruction Formats
8-bit
opcode: machine instruction code (8 bits)
16-bit
opcode: machine instruction code (8 bits)
r1, r2: register identifiers (4 bits, 4 bits)
opcode
opcode
r1
r2

## Slide 20: SIC/XE – Additional Instruction Formats
24-bit
opcode: machine instruction code (6 bits)
flags: n, i, x, b, p, e (6 bits)
disp: 12-bit address displacement
32-bit
opcode: machine instruction code (8 bits)
flags: n, i, x, b, p, e (6 bits)
address: 20-bit address
opcode
opcode
flags
address
flags
disp

## Slide 21: SIC/XE – Instruction Flags
n: Indirect addressing flag
i: Immediate addressing flag
x: Indexed addressing flag
b: Base address-relative flag
p: Program counter-relative flag
e: Format 4 instruction flag

## Slide 22: SIC/XE – Additional Addressing Modes
Base Relative
opcode
b=1, p=0
disp
Address
Operand
Memory Location
B Register
Effective address
+

## Slide 23: SIC/XE – Additional Addressing Modes
Program-Counter Relative
opcode
b=0, p=1
disp
Address
Operand
Memory Location
PC Register
Effective address
+

## Slide 24: SIC/XE – Additional Data Formats
Floating Point (48-bits)
  s: 1-bit
  exponent: 11-bits
  fraction: 36-bits
s
exponent
fraction

## Slide 25: SIC/XE – Instructions (Load & Store)
Transfer 1 word of data (24 bits) between the B, S, or T registers, and a memory location
Transfer 2 words of data (48 bits) between the F register, and a memory location
  STB location
  STS location
  STT location
  LDB location
  LDS location
  LDT location
  LDF location
  STF location

## Slide 26: SIC/XE – Instructions (FP Arithmetic)
Floating point arithmetic involves the F register and a memory location
  ADDF location
  SUBF location
  MULF location
  DIVF location
The contents of the F register are replaced by: F (operation) (contents of location)

## Slide 27: Precision and Portability: (an aside)
In order for programs to be portable across platforms (hardware independent), arithmetic must work the same on any hardware.
Language standards and test suites usually specify a minimum range and precision for each data type… but some systems support greater range and precision.
A program may run correctly on a high-precision system, and fail when run on a lower precision system – even though both systems are standards-compliant. The programmers are inadvertently depending on higher precision than the standards.
Some programs may even fail when running on higher-precision hardware.

## Slide 28: Floating Point Arithmetic
IEEE 754: a set of standards for binary and decimal floating point representation and arithmetic. The standard was established in 1985 and updated in 2008 and 2019.
Each sub-standard specifies the number of bits (digits) and the exponent size.
  binary32: 24 significant bits (including sign); 8 exponent bits

## Slide 29: Floating Point Arithmetic - continued
A floating point format consists of:
  a base (also called radix) b, which is either 2 (binary) or 10 (decimal) in IEEE 754;
  a precision p;
  an exponent range from emin to emax, with emin = 1 − emax for all IEEE 754 formats
  Specified representations for +infinity, -infinity, and NaN (not a number)
The IEEE 754 floating-point standard also includes rules for rounding

## Slide 30: SIC/XE – Instructions (Register Arithmetic)
Perform an arithmetic operation on two specified registers:
  ADDR reg1, reg2: reg2 = reg2 + reg1
  SUBR reg1, reg2: reg2 = reg2 - reg1
  MULR reg1, reg2: reg2 = reg2 * reg1
  DIVR reg1, reg2: reg2 = reg2 / reg1
Logical operations: circular shift the specified register ‘n’ bits
  SHIFTL r1,n: circular shift left
  SHIFTR r1,n: circular shift right
RMO reg1, reg2: Move the first specified register to the second
CLEAR reg1: Clear the specified register (set the value to 0)

## Slide 31: SIC/XE – Instructions (Conversion)
Convert the integer in the A register to floating point, and store the result in the F register
  FLOAT
Convert the floating in the F register to integer, and store the result in the A register
  FIX
Normalize the floating point number in the F register
  NORM

## Slide 32: SIC/XE – Instructions (Comparison)
Comparison instructions set the CC flag to <, =, or >
Compare the F register and the 48-bit contents of a memory location
  COMPF location
Compare the first specified register to the second specified register
  COMPR reg1,reg2
Increment the X (index) register, and compare the result to the contents of a specified register
  TIXR register

## Slide 33: Assembly Example: SIC/XE
Note that the SIC/XE has variable length instructions. This is often true of CISC machines. RISC machines have uniform length instructions.
Line # | Label | Instruction | Argument | Address | Instruction Size*
1 | Program | START | 1000 | 1000 | 0
2 |  | LDA | Inventory | 1000 | 3
3 |  | LDT | Sales | 1003 | 3
4 |  | SUBR | T, A | 1006 | 2
5 |  | J | DisplayRoutine | 1008 | 3
6 | Partnumber | BYTE | C’005740’ | 1011 | 6
7 | Inventory | WORD | 500 | 1017 | 3
8 | Sales | WORD | 27 | 1020 | 3

## Slide 34: Useful Resources
Simplified Instructional Computer (SIC) Architecture
  https://www.geeksforgeeks.org/simplified-instructional-computer-sic/
SIC/XE Architecture
  https://www.geeksforgeeks.org/sic-xe-architecture/
SIC/XE Instruction Set
  https://www.geeksforgeeks.org/instruction-set-used-in-sic-xe/
  https://www.unf.edu/~cwinton/html/cop3601/supplements/test.html

## Slide 35: The SIC/XE Simulator
There is a Simulator for the SIC/XE machine
  Integrated Development Environment
  Assembler
  Linker
  Simulator (executes SIC/XE instructions)
Download at: http://jurem.github.io/SicTools/
  Written in Java
  Download the JAR (Java Archive) file

## Slide 36: Assignment 1
Due in One Week (at start of class)
Log in to Canvas and complete Assignment 1
Recommended: Download and install the SIC/XE simulator