## Slide 1: CMPE 220
Class 5 – Assembly Language & Assemblers

## Slide 2: Using Pseudocode
Fibonacci Sequence
Each number in the sequence is the sum of the previous two:
  0, 1, 1, 2, 3, 5, 8, 13, 21, 34…
Write a short program to print a sequence of Fibonacci numbers
  Also, indicate numbers that are evenly divisible by 5

## Slide 3: Output
Fibonacci Sequence
0: 0 Divisible by 5!
1: 1
2: 1
3: 2
4: 3
5: 5 Divisible by 5!
6: 8
7: 13
8: 21
9: 34
10: 55 Divisible by 5!
11: 89
12: 144
13: 233
14: 377
15: 610 Divisible by 5!
16: 987
17: 1597
18: 2584
19: 4181
20: 6765 Divisible by 5!
21: 10946
22: 17711
23: 28657
24: 46368
25: 75025 Divisible by 5!
26: 121393
27: 196418
28: 317811
29: 514229
30: 832040 Divisible by 5!

## Slide 4: Pseudocode
PRINT "Fibonacci Sequence”
linenumber = 0;
prev_prev = -1;
prev = 1;
WHILE (linenumber <= 30)
{
fib = prev_prev + prev;
PRINT linenumber and fib
IF (fib mod 5 is 0) PRINT “divisible by 5”
PRINT new line
i = i + 1;
prev_prev = prev;
prev = fib;
}

## Slide 5: Compilers Emit Assembly Language Code
Sometimes length and complex instruction sequences are req uired to do things that are not built into the machine architecture

## Slide 6: EXAMPLE: Nesting Subroutines
The SIC instruction set has a subroutine call – JSUB
Because there is only one return address register (L), subroutines cannot be nested:
 | . . . | . . .
 | JSUB | FIRST
 | . . . | . . .
FIRST | . . . | . . .
 | JSUB | SECOND
 | . . . | . . .
 | . . . | . . .
 | RSUB | 
SECOND | . . . | . . .
 | . . . | . . .
 | RSUB | 
3
2
1
4

## Slide 7: A Subroutine Call Stack
SIC/XE has JSUB and RSUB instructions, but only one L register
Nested subroutine calls don’t work!

## Slide 8: EXAMPLE: Nesting Subroutines
The SIC instruction set has a subroutine call – JSUB
Because there is only one return address register (L), subroutines cannot be nested:
 | . . . | . . .
 | JSUB | FIRST
 | . . . | . . .
FIRST | . . . | . . .
 | JSUB | SECOND
 | . . . | . . .
 | . . . | . . .
 | RSUB | 
SECOND | . . . | . . .
 | . . . | . . .
 | RSUB | 
3
2
1
4

## Slide 9: Storage Declarations
SSTACK | RESW | 10 | Allow 10 nested subroutine calls
SINDEX | WORD | 0 | Index
SMAX | WORD | 30 | Stack Maximum
SAVEA | RESW | 1 | Space to save A register (we’ll see why)
SAVEX | RESW | 1 | Space to save X register (we’ll see why)

## Slide 10: Subroutine Call
JSUB | *+3 | Get address into L register
STA | SAVEA | Save the A register
STX | SAVEX | Save the X Register
LDA | SINDEX | Get the stack index in A
COMP | SMAX | See if we’re at the end of stack
JEQ | ERROR | 
RMO | L, A | Move return address into A register
ADD | 35 (?) | Increment address to point past this code
LDX | SINDEX | Get the stack index in X
STL | SSTACK,X | Use indexed addressing to store return address on stack
LDA | #3 | Increment stack index
ADDR | X, A | 
STX | SINDEX | 
LDA | SAVEA | Restore the A register
LDX | SAVEX | Restore the X register
J | SUB | Jump to the subroutine
• • • | • • • | This is where we will return

## Slide 11: Subroutine Return
LDA | SINDEX | Decrement stack index
SUB | #3 | 
STA | SINDEX | 
LDX | SINDEX | 
LDL | SPTR,X | Indexed load to get the return address into L register
LDA | SAVEA | Restore the A register
LDX | SAVEX | Restore the X register
RSUB |  | 

## Slide 12: Managing a Runtime Stack
Many compiled languages use a runtime stack
A “frame” is pushed onto the stack each time a subroutine is called
The frame contains the subroutine parameters, and the local variables
Calling sequence:
  Load A with the number of bytes required
  jsb stkpush
  Returns the address of the stack frame in A
  If the stack is full, returns 0 in A
To “Pop” the frame off the stack
  jsb stkpop

## Slide 13: Memory Management
stack | RESW | 1000 | ; space for stack
endstack | WORD | 0 | ; end of stack
stacktop | WORD | #stack | ; next unused word
stackptr | RESW | 1 | ; stack address pointer
savea | RESW | 1 | ; place to save A register
savex | RESW | 1 | ; place to save X register
Stack frame 1
•••
Stack frame 1 pointer
Stack frame 2
•••
Stack frame 2 pointer
Stack frame 3
•••
Stack frame 3 pointer
Not yet used
stack
stackptr
stacktop

## Slide 14: Memory Management
stkpush | STX | savex | ; save the X register
 | LDX | stacktop | ; get the current top of stack
 | STX | stackptr | ; save it as next stack pointer
 | ADD | stackptr | ; add space needed to stack pointer
 | ADD | #3 | ; add space for previous stack pointer
 | COMP | #endstack | ; check for stack overflow
 | JLT | stkOK | 
 | CLEAR | A | ; return error condition if stack is full
 | RSUB |  | 
stkOK | STA | stacktop | ; update top of stack
 | SUB | #3 | ; get address to store prev stack ptr
 | RMO | X, A | 
 | LDA | stackptr | ; get stack pointer and put in current stack frame
 | STA | 0, X | 
 | LDX | savex | ; restore X
 | RSUB |  | ; return to caller

## Slide 15: Memory Management
stkpop | STA | savea | ; save the A register
 | STX | savex | ; save the X register
 | LDA | stacktop | ; Get the address of the bottom of the previous stack frame
 | SUB | # | 
 | RMO | X, A | ; move it into X
 | LDA | 0, X | ; get the address of the previous stack frame
 | STA | stacktop | ; make it the new top of stack
 | LDA | savea | ; restore A
 | LDX | savex | ; restore X
 | RSUB |  | ; return to caller

## Slide 16: Printing
The compiler emits code to print; this is usually a call to a library routine
As an example, here is a very simple function to print a string
Calling sequence:
  Store the I/O device number in outdev
  Load X with the address of a null-terminates string to print
  jsb pstr

## Slide 17: Printing
outdev | BYTE | 5 | ; Output device number
savea | RESW | 1 | ; Space to save the A register
pstr | STA | savea | ; Save A
 | LDCH | 0, X | ; A = character to output
 | COMP | #0 | ; Check for null character (string terminator)
 | JGT | pstr1 | ; If not null, go print the character
 | LDA | savea | ; If null, all done printing: return A.
 | RSUB |  | ; Return to caller
pstr1 | TD | outdev | ; Test to see if output device is ready
 | JEQ | pstr1 | ; Device not ready
 | WD | outdev | ; Output A register to output device
 | TIX | #0 | ; Increment X to point to next character
 | J | pstr | ; loop

## Slide 18: Assignment 2
Short assignment in Canvas – due next Wednesday
Pseudocode
SIC/XE Assembly Language